Specs SCAG Giant-Vac TLB25-48KBD

- Engine – Kubota 4-cyl. Liquid-cooled

- Horsepower – 48hp

- Fuel – diesel

- Fuel Capacity – 8.5gal

- Frame Construction – All steel, welded

- Housing Construction – All steel, welded 1- gauge

- Housing Design – Removable back panel for easy impeller and wear plate access

- Impeller Construction – 4 blades, ½” thick, all-steel, welded, high CFM, debris reducing design

- Impeller Mounting – Straight bore

- Impeller Diameter – 25”

- Impeller Width – 9”

- Housing Width – 10.5”

- Wear Plates – Yes – ½” steel, bolt-in replaceable

- House Spec. – 16” diameter intake hose, .045 blue polyurethane reinforced with wire helix with wearstrip.  Length 84”.

- CFM output – 7,318 CFM

- Axle – Heavy-duty Dexter Torflex Axle (3,500lb)

- Tires – 205/75 R15

- Trailer Width – 66-3/4”

- Height – 121-1/4”

- Wheel Chocks and Chock boxes – Yes, standard equipment

- Traffic Cones and Cone Holder – Yes, standard equipment

- Hitch – 2-5/16” Ball  Hitch

- Weight – 2,300lbs.

- CA compliant – Yes

- Warranty – 2 Year Commercial